## Slide 1: Video Telematics POC

## Slide 2: Table Of Contents
1
2
3
4
5
3
4
5
6
7
Project Overview
Requirements & Components
Key Features
Firmware Architecture
High-Level Cloud Architecture
5
Description of Modules
8

## Slide 3: Project Overview
Building a Telematics Control Unit that detects driving events through video and sensors. System captures and trims footage around incidents like harsh braking or crashes. Event clips and sensor data automatically upload to Azure Cloud.

## Slide 4: Project Requirements –
Hardware:
- Raspberry Pi 4
- GPS Module
- Accelerometer/IMU (MPU6050)
- USB Camera
MicroSD
Software:
- Python for sensor reading & video handling
- Azure Blob, Cosmos DB, Functions for cloud

## Slide 5: Key Features
Incident Detection: Harsh braking, acceleration, tilt
Location-Based Event Tracking
Continuous video recording & event-based trimming
Auto-upload to Azure Cloud (video + metadata)

## Slide 6: Preliminary Technical Architecture - Firmware
V4L2 (Video4Linux2)
USB/File system
I2C/SPI Driver
Network Stack
UART Driver
GPS Module
IMU Sensor
USB Camera
DRIVER LAYER
Raspberry Pi 4
HARDWARE LAYER
SERVICE LAYER
Video Recorder Service
Event Detection
UART Driver
Video Trimmer
Sensor Reader Service
APPLICATION LAYER
Main Controller
Incident Manager
Alert Notifications
Dashboard (Optional)

## Slide 7: High-level Device Architecture
Raspberry Pi
Camera Module
GPS Module
Accelerometer
Local Storage
Network Interface
Event Detection Module(S/W)
Video Trimming Module
Azure
Wi-Fi / 4G

## Slide 8: Description of modules
GPS Module → Raspberry Pi Continuously sends speed, location, and timestamp data over UART.
Accelerometer (IMU) → Raspberry Pi Sends real-time x/y/z acceleration and tilt data over I2C or SPI.
Camera Module ⇄ Raspberry Pi Streams continuous video; Raspberry Pi manages capture, frame rate, and resolution.
Raspberry Pi → Event Detection Logic (onboard software) Analyzes sensor inputs to detect incidents like harsh braking, acceleration, or tilt.
Event Detected → Trigger Video Trimming Module Extracts a short video clip (e.g., 10s before + 15s after the event).
Trimmed Clip → Local Storage Temporarily stores the video file and incident metadata (JSON/log).
Raspberry Pi → Network Module (Wi-Fi / 4G Dongle) Connects to the internet for uploading data to the cloud.
Trimmed Video + Metadata → Azure Cloud Uploaded to Azure Blob Storage (video) and Cosmos DB (event info) via API or IoT Hub.

## Slide 9
Raspberry Pi
GPS
Accelerometer
Camera
Storage
Hardware
Location Information
Sensor Data Collection
Event Detection Module
Cloud Uploader
Continuous Video Buffer
Software
Motion Data
Video Footage
Video Data Management
Processed Sensor Data
Video Trimming Module
Event Detection Trigger
Trimmed Clip & Meta Data
Video Segments
Azure IoT Hub
Azure Functions
Azure Blob
Storage
Azure Cloud
Video & Meta Data
Event Data

## Slide 10: Description of modules
GPS Module : Continuously sends speed, location, and timestamp data over UART.
Accelerometer (IMU) : Detects motion changes (e.g., harsh braking), and this data is gathered by the Raspberry Pi.
Camera Module : Records continuous video , which is stored in a circular buffer on the Raspberry Pi to manage storage efficiently..
Storage : The Continuous Video Buffer interacts with the storage (e.g., SD card) to save video footage and retrieve segments when needed, such as during trimming. This bidirectional flow ensures the buffer can update storage and access it as required.
Software Processing
Sensor Data Collection → Event Detection Module:
  The Sensor Data Collection module aggregates and processes the raw data, then passes it to the Event Detection Module to identify events like sudden braking or accidents.

## Slide 11
Event Detection Module → Video Trimming Module:
  When the Event Detection Module identifies an event, it notifies the Video Trimming Module to extract a relevant video clip.
Video Trimming Module ↔ Continuous Video Buffer:
  The Video Trimming Module accesses the Continuous Video Buffer to retrieve a 25-second video segment (e.g., 15 seconds before and 10 seconds after the event) and may update the buffer’s state during this process.
Video Trimming Module → Cloud Uploader:
  After trimming the video, the module sends the resulting clip and associated metadata to the Cloud Uploader for transmission.
Cloud Uploader → Azure:
  The Cloud Uploader transmits the processed data to Azure for storage and further processing (e.g., via Azure IoT Hub to Blob Storage).

## Slide 12
Thank You
www.global-csg.com